Overview
Content:
Arduino
MIDI
Arduino as MIDI Controller
Sources

---
1. Arduino
Arduino =
+
(Hardware: Mikrokontroller + Board)
(Software: IDE + Programming Lang.)

---
1. Arduino - Hardware
e.g.: PC, MIDI, ...
UART (Serial over USB)
e.g.:
Sensors,
Triggers,
Switches
...
Digital Pins
Analog Pins
e.g.:
Sensors,
Potentiom.,
...
Digital Pins
e.g.:
Motors
Servos
Lamp
...

---
2. MIDI (Musical Instrument Digital Interface)
- Hardware:
  - UART (Universal Asynchronous Receiver Transmitter): „Serial Port“
  - 5V
  - 31250 bit/sec: 1 bit takes 32us (=0.000032s)
  - Unidirectional: a single cable only transmitts data in one direction
  - 5pin DIN connectors

---
2. MIDI Wiring
Sender, e.g. Keyboard
Receiver, e.g. Synthesizer

---
2. MIDI Protocol
MIDI Message = status byte + 2 data bytes
Details:
	Byte 0 (status)	Byte 1 (data)	Byte 2 (data)
Notes:	Starts with 1, so values are in 8016...FF16	Starts with 0, values in 016...7F16	Starts with 0, values in 016...7F16
Note Off:	8n16 (n: channel from 0..15)	kk (pitch)	vv (velocity)
Note On:	9n16 (n: channel from 0..15)	kk (pitch)	vv (velocity)
...	...	...	...

---
2. MIDI Protocol - Example
...,100100002, 001111002, 011111112, ...
= 916
(note on)
= 0
(chan. 0)
= 3C16
= 6010
(Middle c)
= 7F16
= 12710
(max. vel.)
Starts with 1
→ status byte

---
3. Arduino as MIDI Controller - Concept
PC
(Via MIDI over USB, using USBMidiKliK)
UART 0
UART 1
Additional MIDI devices via DIN-5
Analog Pins
Digital Pins
Potentiometers
(optional: foot pedals)
Triggers,
Switches

---
3. Arduino as MIDI Controller
- Hardware Components:
  - Arduino Mega 2560 (lots of IO interfaces compared to Arduino Uno)
  - Box
  - Potentiometers, Triggers, Switches
  - Drill, Solder Iron, ...
- Software:
  - USBMidiKliK: USB Firmware to turn Arduino into a MIDI-over-USB device
  - Own code

---
3. Arduino as MIDI Controller - Wiring

---
3. sgDevice 2 – Live Demo
LIVE DEMO

---
4. Sources
- Sources:
  - Arduino Webpage: https://www.arduino.cc
  - Wikipedia on MIDI: https://de.wikipedia.org/wiki/Musical_Instrument_Digital_Interface
  - Microcontroller.net on MIDI:https://www.mikrocontroller.net/articles/MIDI
  - Project repository of my project: https://github.com/EsGeh/sgDevice
  - UART Firmware (turn Arduino into a MIDI device): https://github.com/TheKikGen/USBMidiKliK
- Image sources:
  - https://store.arduino.cc/arduino-uno-rev3
  - https://www.theengineeringprojects.com/2018/10/introduction-to-arduino-ide.html
  - https://de.wikipedia.org/wiki/DIN-Steckverbinder
  - https://www.midi.org/specifications/item/midi-din-electrical-specification